## Slide 1: BIAPT Lab Meeting
Work in Progress
Wednesday, February 24th

## Slide 2: Research Line 1: To use electroencephalography (EEG) to elucidate novel biomarkers of concussion and understand the electrophysiological basis of clinical impairments.
Notes: Concussion diagnosis and management is currently focused on clinical assessment, particularly computerized neurocognitive testing.
  Little physiological data used
  Relationships between physiological data and clinical outcomes largely unexplored
Spectral EEG analyses quantify the oscillatory power of the brain’s electrical activity across varying frequencies.
-Spectral deficits observed post-concussion
-Major of rs-EEG literature in concussion use spectral analysis
Functional connectivity may be a better outcomes
  -Diffuse axonal injury- connectivity may more precisely measure disrupted neural communication
  -Research suggests functional connectivity markers are altered post-concussion19-21 and are a larger contributor to a proprietary concussion classification algorithm than spectral markers.22,23
Came to Stefanie to learn new EEG skills, that I can then take back to individuals with concussion

## Slide 3: The Reconstructing Consciousness and Cognition (ReCCognition) Study sought to measure the sequence of cognitive recovery following emergence from anesthesia. .
Maier et al. 2017; Rokos et al.
Notes: 3 locations (Michigan, UPenn, Washington University in St. Louis
Participants were randomized to anesthesia received propofal and were under anesthetics for 3 hours
Control group received no intervention, but were required to remain awake during 3 hours block (TV read)
In total, 15 participants (9 anesthesia, 6 controls) were available to be used

## Slide 4: A modified version of the Cognition Test Battery for Spaceflight was administered at all eight sessions.
Maier et al. 2017; Rokos et al.
Notes: 3 locations (Michigan, UPenn, Washington University in St. Louis
Participants were randomized to anesthesia received propofal and were under anesthetics for 3 hours
Control group received no intervention, but were required to remain awake during 3 hours block (TV read)
In total, 15 participants (9 anesthesia, 6 controls) were available to be used

## Slide 5: Motor Praxis
Domain: sensorimotor speed
Click on squares randomly appearing on screen
  Each successive square gets smaller
  20 squares in each session
Basner et al. 2015

## Slide 6: Visual Object Learning Test
Domain: memory
10 3D figures are sequentially displayed
  Memorize
  Recall 10 target figures from a set of 20
Basner et al. 2015

## Slide 7: Fractal N-Back (2-Back)
Domain: working memory
Images presented sequentially every 750ms
  Respond when image is the same as image displayed two times ago
  62 images per session
Basner et al. 2015
6
4
6
2
1
5
2

## Slide 8: Abstract Matching
Domain: executive function
Two pairs of objects at the bottom, varied on color and dimension
Target object presented in the middle
  Classify based on rules provided
Basner et al. 2015

## Slide 9: Psychomotor Vigilance Test
Domain: vigilant attention
Timer randomly appears and starts counting
  Hit space bar as quickly as possible
  Test lasts for 3 minutes
Basner et al. 2015

## Slide 10: Digit Symbol Substitution Test
Domain: working memory, visual search
Symbol appears on screen
  Use legend at bottom to select corresponding number
  As many symbols as possible in 90 seconds
Basner et al. 2015

## Slide 11: Subjects were fitted with high-density EEG (128 electrodes) throughout the entire study period.
Maier et al. 2017
Notes: For our study, we focused on the EEG recorded during all six cognitive tests, over the 8 administrations

## Slide 12: Can graph theory features accurately classify the recovery of cognition in adults following an experimental anesthesia protocol compared to healthy controls?
  Graph theory metrics: path length, modularity, clustering coefficient, global efficiency
  Frequency bands: theta, alpha, beta
  Receiver operating curve analyses
    Data set too small for machine learning
Notes: Theta modularity maximally classified between the anesthesia and control groups immediately post-intervention (sensitivity= 85.7%; specificity= 61.1%; AUC= 0.72; 2(1)=12.21; p<0.001; Figure 1). AUC decreased over time and returned to baseline levels (AUC=0.54) by 90mins post-intervention.

## Slide 13: Step 1: Pre-process the data in EEGlab
Data already cleaned
Load dataset
Add channel locations
Removed non-scalp channels
  Not aware there was code to filter these channels out later
Add start/stop times for each cognitive test
Epoch data
  5 seconds after test start to test end
Save epoch as .mat file
Notes: 5 seconds after- start time was was when test began, but there are directions
5 seconds was conservation estimate that we were using data collected during the test only, not the direction

## Slide 14: Step 2: Run wPLI analysis
Analysis run in EEGApp
Parameters
  Length of segment: 10
  Number of permutations: 20
  P value: 0.05
  Bandpass
    Delta: 1-4Hz
    Theta: 4-8Hz
    Alpha: 8-13Hz
    Beta: 13-30Hz
Electrode order updated
Baseline
Immediately Post-Anesthesia
Notes: dPLI was also conducted, but graph theory is based on wPLI so that’s what I’m focusing on

## Slide 15: Step 3: Sweep data to determine threshold
Reduce matrix to 85x85
  Channels available across all 15 participants
Threshold sweep
  Minimally spanning map
  0.90-0.01 by 0.01 steps
Average data
  Mean from all six cognitive tests from the first administration (baseline)
  Thresholds calculated separately for each frequency band

## Slide 18: Step 4: Create a binary matrix
Applied individual network threshold
wPLI values > threshold = 1
  I.e. Threshold = 0.20, wPLI in top 20% of data were set to 1
Otherwise, binary matrix= 0

## Slide 19: Step 5: Create null networks/random networks
Parameters
  Function: randomizer_bin_und.m
  Fraction of edges to rewire: 10%
  Number of null networks created: 100

## Slide 20: Step 6: Calculate global efficiency (and other variables)
Load binary network and null networks
Code: binary_global_efficinecy.m

## Slide 21: The problem: roughly 5% of global efficiency values are above 1; this is theoretically not possible.
Notes: 81 (out of 2074- roughly 5%) global efficiency outcomes are greater than 1
-19 of the 81 are 1.01 or greater
-0 are greater than 1.1
All other outcomes (path length, clustering characteristics, small-worldness)
SAS- get freq/percentages about number of participants with outcomes greater than 1, 1.01
  Participants
  Cognitive test
  Time (cogtest 1, cogtest 2, etc.)

## Slide 22: Efficiency values ≥ 1 appear to be less common in the beta frequency band compared to alpha and theta.

## Slide 23: Global efficiency values above 1 are more common in the anesthesia group, although every participant but one has at least one efficiency values ≥ 1.

## Slide 24: Things I have (unsuccessfully) tried to resolve this issue:
Null network code
  Different functions
  Adjusting parameters within a function
Global efficiency code
Network threshold
  Individual vs. constant values
Re-running the analysis
  Generating wPLI matrices via code
Notes: Note: only tried these work arounds a subset of the data, but as it didn’t resolve issues in the subset I didn’t both re-running data in the full set

## Slide 25: Things I have (unsuccessfully) tried to resolve this issue:
Null Network Code
  Different functions
  Adjusting parameters within a function
Global efficiency code
Network Threshold
  Individual vs. constant values
Re-running the analysis
  Generating wPLI matrices via code
Notes: Note: only tried these work arounds a subset of the data, but as it didn’t resolve issues in the subset I didn’t both re-running data in the full set

## Slide 26: Using different null network codes did not produce any meaningful changes.

## Slide 27
Null_model_und_sign
Null_model_dir_sign
Randmio_dir_connected
Randmio_dir_sign
For the most part, global efficiency values remained above one regardless of which null network code was utilized.
Changes to global efficiency values were extremely small regardless of which function was used.

## Slide 28
Danielle’s code from Motif Paper
My code
Notes: https://github.com/BIAPT/EEGMotifs/blob/master/src/features/calculate_validated_motifs.m

## Slide 29: Things I have (unsuccessfully) tried to resolve this issue:
Null Network Code
  Different functions
  Adjusting parameters within a function
Global efficiency code
Network Threshold
  Individual vs. constant values
Re-running the analysis
  Generating wPLI matrices via code
Notes: Note: only tried these work arounds a subset of the data, but as it didn’t resolve issues in the subset I didn’t both re-running data in the full set

## Slide 30: Altering the fraction of edges to rewire provided no meaningful difference.
5%
10%
20%
Notes: Random_bin_und
Individual threholds

## Slide 31: Frequency of weight sorting in null_dir_sign.m also did not appear to make a meaningful difference.
0.1
0.25
Notes: 10% rewiring kept throught
Random_bin_und

## Slide 32: Changing the number of null networks generally reduces the global efficiency values, but some cells are still above 1.
10
100
Notes: Original told that for pubs, you want 100+ null networks
Danielle’s code only uses 10 null networks

## Slide 33: Things I have (unsuccessfully) tried to resolve this issue:
Null Network Code
  Different functions
  Adjusting parameters within a function
Global efficiency code
Network Threshold
  Individual vs. constant values
Re-running the analysis
  Generating wPLI matrices via code
Notes: Note: only tried these work arounds a subset of the data, but as it didn’t resolve issues in the subset I didn’t both re-running data in the full set

## Slide 34
Danielle’s code from AEC
Yacine’s Matlab function

## Slide 35: Things I have (unsuccessfully) tried to resolve this issue:
Null Network Code
  Different functions
  Adjusting parameters within a function
Global efficiency code
Network Threshold
  Individual vs. constant values
Re-running the analysis
  Generating wPLI matrices via code
Notes: Note: only tried these work arounds a subset of the data, but as it didn’t resolve issues in the subset I didn’t both re-running data in the full set

## Slide 36: Altering the threshold value moved some global efficiency values to under 1, but increased other values over 1.
Individual
35%
25%
Notes: 10% rewiring kept throught
Random_bin_und

## Slide 37: Things I have (unsuccessfully) tried to resolve this issue:
Null Network Code
  Different functions
  Adjusting parameters within a function
Global efficiency code
Network Threshold
  Individual vs. constant values
Re-running the analysis
  Generating wPLI matrices via code
Notes: Note: only tried these work arounds a subset of the data, but as it didn’t resolve issues in the subset I didn’t both re-running data in the full set

## Slide 38
Step 1: Pre-process data
Step 2: Run wPLI analysis
Step 3: Threshold Sweep
Step 4: Create binary matrix
Step 5: Create null networks
Step 6: Calculate global efficiency
Changes made:
wPLI step size: 1 to 10
Threshold: 0.3 to individual value

## Slide 39: Potential reasons for problems
Data recording during cognitive tasks?
  (I think) Other data from MDF data is from resting-state conditions
  Same issue on DSI-24 which was collected during resting state
Removed non-scalp electrodes while cleaning in EEGlab?
  Those electrodes get filtered out anyway
  Bad channels removed in resting-state data which works
  Same issue on DSI-24 data with only one bad channel removed
Issues with reduced 85x85 channel PLI matrix?
  Re-running the analysis: used all available channels for each participant and issue remains
Some sort of statistical anomaly/rounding error?

## Slide 40
Notes: Resting state fMRI data
-ROI to ROI connectivity matrix with a Fischer’s transform
-due to the complex math and transformations, they get values over 1 even though they theoretically shouldn’t
-All values in question for were ~1.0039 etc. so kind of negligible decimal values and very close to 1 so he said it was ok to keep them bc the decimal stuff was just bc of all the math
Everyone else has been able to resolve the issue

## Slide 41: Any thoughts or suggestions? Did you notice any errors in the code?
Notes: Thoughts? Suggestions? Errors